Now I have everything. Let me write the full document.

# Laser Controller — Point-to-Voltage Data Path
## Complete Technical Reference

## Block Diagram
Application Code
    │
    │ std::vector<LaserPoint> (normalized float, [-1,1])
    ▼
HeliosOutput::SendFrame()
    │
    │ ScaleToILDA() float → 12-bit ILDA integers
    │ BuildFrame() add transitions, dwell, blanking
    │ ResampleToCount() budget enforcement
    │
    ▼ std::vector<HeliosPoint> (12-bit XY, 8-bit RGBI)
Queue (max 2 frames, thread-safe)
    │
    ▼
DacThreadFunc()
    │ polls helios_.GetStatus(0) → blocks until DAC ready
    │
    ▼
HeliosDac::WriteFrame()
    │
    │ Packs 7 bytes per point
    │ Appends 5-byte trailer (PPS, count, flags)
    │
    ▼ USB Bulk Transfer (EP 0x02)
    │
    ▼
SAM4S2B Firmware (112 MHz ARM Cortex-M4)
    │ USB interrupt → frame buffer
    │ SysTick fires at PPS rate
    │ point_output() called each tick
    │
    ├── DACC (dual channel, 12-bit)
    │ Pin PA17 → X galvanometer driver
    │ Pin PA18 → Y galvanometer driver
    │
    └── SPI @ 22.4 MHz → DAC084S085
        → Red laser diode driver
        → Green laser diode driver
        → Blue laser diode driver
        → Intensity (master)

## Layer 1 — Application: LaserPoint
The entry point for all laser output is HeliosOutput::SendFrame(), which takes a list of polylines, each a std::vector<LaserPoint>:
struct LaserPoint {
    float x, y; // −1.0 = galvo minimum, +1.0 = galvo maximum
    float r, g, b; // 0.0 = laser off, 1.0 = full intensity
};
The coordinate system is centred on the projection surface. The Y axis is up (matching mathematical convention). This is the only place in the chain where floating-point normalized values exist.
The application calls one of three entry points:
- SendFrame(vector<vector<LaserPoint>>) — multiple explicit polylines
- SendPolyline(vector<LaserPoint>) — single continuous stroke (calls SendFrame internally)
- SendPointCloud(vector<LaserPoint>, gapThreshold) — auto-segments on distance gaps

## Layer 2 — HeliosOutput Processing
All three entry points funnel into BuildFrame(), which is the heart of the software layer. Before it runs, coordinates are converted.
### 2.1 ScaleToILDA — Float → Integer
// X: normalized [-1.0, 1.0] → ILDA [0, 4095]
hp.x = clamp( (int)((p.x + 1.0f) * 0.5f * 4095), 0, 4095 );
hp.y = clamp( (int)((p.y + 1.0f) * 0.5f * 4095), 0, 4095 );
hp.r = clamp( (int)(p.r * 255), 0, 255 );
hp.g = clamp( (int)(p.g * 255), 0, 255 );
hp.b = clamp( (int)(p.b * 255), 0, 255 );
hp.i = max(hp.r, max(hp.g, hp.b)); // intensity = dominant channel
After this step everything is integer. The HeliosPoint struct holds 12-bit XY (stored in uint16_t) and 8-bit RGBI.

### 2.2 Budget Distribution
Before building the frame, the PPS budget is allocated across polylines:
totalBudget = max_pps / target_fps e.g. 30000 / 30 = 1000 points
overhead = Σ transition cost per polyline
        (blank_pts + pre_on_pts + post_on_pts + travel_pts)
drawBudget = totalBudget − overhead
Each polyline is resampled to a share of drawBudget proportional to its arc length. This ensures longer polylines get more fidelity and shorter ones don't crowd the budget. ResampleToCount() does arc-length-parameterised linear interpolation — it computes cumulative path lengths and then steps evenly along the path, not just between vertex indices.

### 2.3 BuildFrame — The Full Assembly
BuildFrame() produces the exact sequence of HeliosPoint values that the firmware will play back, one per SysTick interrupt. The sequence for each polyline is:
┌─ Blanked eased move ──────────────────────────────────────────┐
│ CalcTravelPoints(currentPos, polyStart) points │
│ Quintic ease-in-out interpolation from current → polyStart │
│ Laser OFF (r=g=b=i=0) │
└───────────────────────────────────────────────────────────────┘
┌─ Blank dwell at start ──────────────────────────────────────┐
│ blank_points (default 20) points at polyStart, laser OFF │
│ Purpose: galvo settles at the start position before laser on│
└─────────────────────────────────────────────────────────────┘
┌─ Pre-on dwell ────────────────────────────────────────────────┐
│ pre_on_points (default 8) at polyStart, LASER ON │
│ Purpose: beam reaches full brightness while galvo is still │
└───────────────────────────────────────────────────────────────┘
┌─ Polyline points ─────────────────────────────────────────────┐
│ All resampled points, laser ON │
│ At each interior vertex: │
│ angle = acos(dot product of adjacent edge unit vectors) │
│ if angle > curve_threshold (20°): │
│ dwell = lerp(angle, 20°→180°, 0→max_vertex_hold) points │
│ Inserted as repeated copies of the vertex point │
└───────────────────────────────────────────────────────────────┘
┌─ Post-on dwell ───────────────────────────────────────────────┐
│ post_on_points (default 8) at polyEnd, LASER ON │
└───────────────────────────────────────────────────────────────┘
┌─ Blank dwell at end ──────────────────────────────────────────┐
│ blank_points (default 20) at polyEnd, laser OFF │
│ Purpose: beam is off before galvo begins next travel │
└───────────────────────────────────────────────────────────────┘
currentPos ← polyEnd
Repeat for every polyline in the frame.
Starting position: BuildFrame reads lastEndX_ and lastEndY_ (atomic ints updated by DacThreadFunc after the previous frame is sent). This means the eased travel on the first polyline begins from where the galvo physically is, not from an assumed center. For a repeated frame like the alignment circle, the galvo ends at the circle start — next frame the travel distance is zero and there is no per-frame lurch.
Quintic ease-in-out (used for blank travel):
t < 0.5 : f(t) = 16t⁵
t ≥ 0.5 : f(t) = 0.5 × (2t−2)⁵ + 1
This starts and ends at zero velocity, preventing galvo overshoot on long blank jumps.

### 2.4 Threading — Queue and DAC Thread
SendFrame() calls BuildFrame() on the calling thread, then pushes the completed vector<HeliosPoint> to a thread-safe queue:
while (frameQueue_.size() > 2) frameQueue_.pop(); // cap at 2
frameQueue_.push(move(frame));
DacThreadFunc() runs on its own thread and does:
loop:
    if not connected → drain queue, sleep 50ms, continue

    status = helios_.GetStatus(0)
    if status < 0 → disconnect, continue
    if status != 1 → not ready, spin-poll

    take frame from queue (re-send last frame if queue empty)

    store frame.back().x → lastEndX_
    store frame.back().y → lastEndY_

    pps = clamp(numPoints × target_fps, min_pps, max_pps)
    helios_.WriteFrame(0, pps, HELIOS_FLAGS_SINGLE_MODE, data, size)
The critical synchronisation: the thread spin-polls GetStatus until the DAC firmware returns 1 (ready). This means no frame can be pushed to the DAC faster than the DAC can play the previous one. HELIOS_FLAGS_SINGLE_MODE tells the firmware to play the frame once and then set status=ready.

## Layer 3 — HeliosDac Library: USB Encoding
HeliosDac::WriteFrame() forwards to HeliosDacUsbDevice::SendFrame(), which encodes the point array into a USB payload and submits it via bulk transfer.
### 3.1 Point Encoding — 7 Bytes Per Point
Each HeliosPoint is packed into exactly 7 bytes:
Byte 0: X[11:4] (upper 8 bits of 12-bit X)
Byte 1: X[3:0] << 4 | Y[11:8] (lower 4 bits X, upper 4 bits Y)
Byte 2: Y[7:0] (lower 8 bits of 12-bit Y)
Byte 3: R (8-bit red)
Byte 4: G (8-bit green)
Byte 5: B (8-bit blue)
Byte 6: I (8-bit intensity / master)
X and Y are encoded in big-endian, packed-nibble format across bytes 0–2. This fits two 12-bit values into 3 bytes with no wasted bits.
### 3.2 Frame Trailer — 5 Bytes
After all point data, the library appends a 5-byte trailer:
Bytes [n×7 + 0..1]: PPS (uint16, little-endian)
Bytes [n×7 + 2..3]: Point count (uint16, little-endian)
Byte [n×7 + 4]: Flags
The firmware reads this trailer to know how fast to run the SysTick and how many points are in the buffer.
### 3.3 Automatic Resampling in the SDK
Before encoding, the library handles two edge cases:
- Too few points for requested PPS: duplicate points to fill the frame
- Frame too large (> MAXFRAMESIZE = 4096): subsample and scale PPS down proportionally
- Firmware alignment bug workaround: if (numPoints − 45) % 64 == 0, reduce by 1 point (avoids a known firmware buffer boundary issue)
### 3.4 USB Transfer
Endpoint: EP_BULK_OUT = 0x02
Direction: Host → Device
Type: Bulk (reliable, not isochronous)
Max frame: 4096 points × 7 bytes + 5 = 28,677 bytes
The USB bulk transfer is blocking (synchronous from the library's perspective). The transfer completes when the OS confirms the data reached the device — not when the firmware finishes playing it.

## Layer 4 — USB Transport
The Helios identifies itself as:
- VID: 0x1209 (pid.codes community VID)
- PID: 0xE500
- Class: Vendor-specific
Four endpoints are active:
Endpoint	Direction	Type	Purpose
0x02	Host→Device	Bulk	Frame data
0x06	Host→Device	Interrupt	Control commands
0x83	Device→Host	Interrupt	Status responses
0x81	Device→Host	Bulk	(unused in normal operation)

Control commands sent to 0x06:
- 0x01 STOP — blank output, center galvos
- 0x02 SHUTTER — toggle mechanical shutter GPIO
- 0x03 STATUS — arm next bulk receive, reply with ready/busy
- 0x04 GET_FIRMWARE_VER — returns 0x06
- 0x05 GET_NAME — reads stored device name from flash
- 0x06 WRITE_NAME — writes name to flash user signature area
- 0xDE ERASE_FIRMWARE — clears GPNVM boot bit → SAM-BA bootloader

## Layer 5 — Firmware (SAM4S2B)
### 5.1 Hardware
MCU: Atmel SAM4S2B — ARM Cortex-M4 at 112 MHz
- 2-channel 12-bit DACC (Digital-to-Analog Converter Controller) — the galvo outputs
- SPI master at 22.4 MHz — the laser colour outputs
- USB Device peripheral
- Timer Counter TC0 — delayed-stop timing
- Flash with User Signature area — device name storage
### 5.2 Reception — Bulk Interrupt Handler
When the OS bulk transfer completes, the firmware USB interrupt fires:
1. Validate payload length: must be (numPoints × 7 + 5) bytes, numPoints ≤ 4096
2. Parse trailer: read PPS and point count from the last 5 bytes
3. If currently idle: copy directly to active frame buffer, call speed_set(pps), set framePos = 0, set frameSize = numPoints × 7
4. If currently playing: copy to the alternate buffer (newFrameReady = true)
5. Arm the bulk endpoint to receive the next frame
Two frame buffers of 4096 × 7 = 28,672 bytes each are maintained for double-buffering — one plays while the other receives.
### 5.3 SysTick — The Heartbeat
void speed_set(uint32_t rate) {
    if (rate > 65535) rate = 65535;
    if (rate < 7) rate = 7;
    SysTick_Config( sysclk_get_cpu_hz() / rate + 1 );
}
// At 112 MHz and 30000 PPS: reload = 112,000,000 / 30,000 = 3,734 ticks
// SysTick fires every 33.3 µs → 30,000 times per second
The SysTick interrupt is configured at higher priority than the USB interrupt. This prevents USB processing from delaying a point output tick, which would cause timing jitter visible as galvo distortion.
On every SysTick:
void SysTick_Handler(void) {
    if (framePos >= frameSize) {
        if (newFrameReady) {
        swap buffers;
        framePos = 0;
        newFrameReady = false;
        } else {
        framePos = 0; // loop current frame
        }
    }
    point_output(&frameBuffer[framePos]);
    framePos += 7;
}
If no new frame arrives, the current frame loops continuously. This is why the alignment circle keeps spinning without the application needing to send frames at 30fps.
### 5.4 point_output — The Final Dispatch
This function executes every 33.3 µs (at 30 kpps). It reads 7 bytes from the frame buffer and writes them to two hardware peripherals simultaneously:
#### DACC Write (Galvanometer XY)
The two DACC channels share a single 32-bit write register. The SAM4S2B DACC supports a packed word write to update both channels in one operation:
// frameBuffer layout: [X_high, X_low|Y_high, Y_low, R, G, B, I]
uint16_t X = (frame[0] << 4) | (frame[1] >> 4); // 12-bit X
uint16_t Y = ((frame[1] & 0x0F) << 8) | frame[2]; // 12-bit Y

// Write both DACC channels (WORD mode, TAG=1 selects channel via data bits)
uint32_t posData = ((uint32_t)(1 << 12 | X) << 16) | (1 << 12 | Y);
dacc_write_conversion_data(DACC, posData);
The DACC reference voltage is 3.3 V. The output range is therefore:
- Value 0x000 → 0.0 V (minimum galvo deflection, ILDA −32767)
- Value 0x800 → 1.65 V (galvo centre)
- Value 0xFFF → 3.3 V (maximum galvo deflection, ILDA +32767)
The DACC drives the input of the galvanometer amplifier boards directly. The amplifiers have their own gain and offset adjustments (hardware trim pots on the galvo driver board) that map this 0–3.3 V range to the ±5 V or ±10 V differential that the galvo coil actually sees.
#### SPI Write (Laser RGB + Intensity)
Four 16-bit SPI transfers are issued in sequence:
// SPI clock: 112 MHz / 5 = 22.4 MHz
// 16-bit word: upper 4 bits = channel/control, lower 12 bits = data (8-bit value << 4)
spi_write(SPI, (R << 4) | (0b1101 << 12), 0, 0); // Red channel
spi_write(SPI, (G << 4) | (0b1001 << 12), 0, 0); // Green channel
spi_write(SPI, (B << 4) | (0b0101 << 12), 0, 0); // Blue channel
spi_write(SPI, (I << 4) | (0b0001 << 12), 0, 0); // Intensity (master)
The target IC is the DAC084S085 — a quad 8-bit SPI DAC. The upper 4 bits encode the destination channel and write mode. The lower 12 bits are left-shifted 8-bit data (value << 4, placing the MSB at bit 11). For a blank point where R=G=B=I=0, all four SPI writes output 0x0000 — this drives the laser DAC to zero volts, turning off the diodes entirely.
At 22.4 MHz and 16-bit transfers with chip-select overhead, all four writes complete in approximately 3 µs — well within the 33.3 µs SysTick period at 30 kpps.

## Layer 6 — Hardware: Voltage to Motion
### 6.1 Galvanometer Chain
SAM4S2B DACC output (PA17 / PA18)
    → 0 to 3.3 V, 12-bit, ~1 µs settling
    ↓
Galvanometer driver board (e.g. ILDA-compatible servo amplifier)
    → Maps 0–3.3 V input to ±5 V or ±10 V differential drive
    → Closed-loop PID servo with position feedback sensor
    ↓
Galvanometer motor coil
    → Current-driven rotary voice coil actuator
    → Mirror on shaft rotates ±20°–±40° depending on model
    ↓
Mirror deflects laser beam
    → X galvo: horizontal axis
    → Y galvo: vertical axis
The galvo driver board's servo bandwidth (typically 2–5 kHz small-signal, less for large deflections) is the fundamental limiting factor in the whole chain. Every blank dwell, pre-on dwell, and corner dwell in BuildFrame exists to give the galvo mechanical settling time within this bandwidth constraint.
### 6.2 Laser Colour Chain
DAC084S085 output (4 channels, 0–3.3 V, 8-bit)
    → Red output → Red laser diode driver (ILDA pin 1/13)
    → Green output → Green laser diode driver (ILDA pin 4/16)
    → Blue output → Blue laser diode driver (ILDA pin 7/19)
    → Intensity output → Optional master intensity / AOM
The ILDA-25 connector pinout used:
ILDA Pin	Signal
1	X+ (galvo X positive)
14	X− (galvo X negative / GND reference)
2	Y+ (galvo Y positive)
15	Y− (galvo Y negative / GND reference)
3	Interlock A (safety loop)
16	Interlock B
4	Intensity / Blanking
17	Intensity return
13	Red+
7	Green+
8	Blue+

The Helios hardware drives these through the DAC084S085 DAC → laser driver amplifiers on the projector side. Blanking is achieved entirely by setting the RGB and I values to zero — the firmware does not use a separate blanking signal line.

## Numeric End-to-End Example
Drawing one point at laser position (0.5, −0.25), full red, from an initial galvo position at centre:
Step 1 — Application
LaserPoint { x=0.5, y=−0.25, r=1.0, g=0.0, b=0.0 }
Step 2 — ScaleToILDA
X = (0.5 + 1.0) * 0.5 * 4095 = 0.75 * 4095 = 3071 (0xBFF)
Y = (−0.25 + 1.0) * 0.5 * 4095 = 0.375 * 4095 = 1535 (0x5FF)
R = 255, G = 0, B = 0, I = 255
Step 3 — BuildFrame (starting from centre 2048,2048)
Travel points: distance ≈ sqrt((3071−2048)²+(1535−2048)²) ≈ 1146 ILDA units
CalcTravelPoints: 1146 / 100 ≈ 11 points, clamped to [8,80] = 11
Frame sequence:
  11 blanked eased-move points (centre → 3071,1535)
  20 blank dwell at (3071, 1535)
   8 pre-on dwell at (3071, 1535), RED
   1 draw point (3071, 1535), RED
   8 post-on dwell at (3071, 1535), RED
  20 blank dwell at (3071, 1535)
Total: 68 points
Step 4 — USB encoding (the draw point, bytes 40–46 of payload)
Byte 0: 0xBF (X[11:4] = 0xBFF >> 4 = 0xBF)
Byte 1: 0xF5 (X[3:0]=0xF, Y[11:8]=0x5 → 0xF<<4 | 0x5 = 0xF5)
Byte 2: 0xFF (Y[7:0] = 0xFF)
Byte 3: 0xFF (R = 255)
Byte 4: 0x00 (G = 0)
Byte 5: 0x00 (B = 0)
Byte 6: 0xFF (I = 255)
Trailer appended: PPS=1000 (LE: 0xE8,0x03), count=68 (LE: 0x44,0x00), flags=0x00.
Step 5 — Firmware receives
Bulk transfer: 68×7 + 5 = 481 bytes
Firmware parses: PPS=1000, numPoints=68
speed_set(1000): SysTick reload = 112,000,000 / 1000 = 112,000
        SysTick fires every 1 ms
Step 6 — SysTick plays the draw point (tick 40 of 68)
frameBuffer[280..286] = [0xBF, 0xF5, 0xFF, 0xFF, 0x00, 0x00, 0xFF]

DACC write:
  X = (0xBF << 4) | (0xF5 >> 4) = 0xBFF = 3071
  Y = ((0xF5 & 0x0F) << 8) | 0xFF = 0x5FF = 1535
  posData = (1<<12 | 3071)<<16 | (1<<12 | 1535)
  dacc_write_conversion_data(DACC, posData)
  → PA17 outputs 3071/4095 × 3.3V = 2.474 V (X)
  → PA18 outputs 1535/4095 × 3.3V = 1.237 V (Y)

SPI writes:
  Red: (255 << 4) | (0b1101 << 12) = 0xDFF0
  Green: (0 << 4) | (0b1001 << 12) = 0x9000
  Blue: (0 << 4) | (0b0101 << 12) = 0x5000
  Intensity: (255 << 4) | (0b0001 << 12) = 0x1FF0
  → DAC084S085 outputs 2.474 V on red channel, 0 V on green/blue
Step 7 — Hardware
X galvo driver: 2.474 V input → amplified to ~+4.95 V coil drive
Y galvo driver: 1.237 V input → amplified to ~−1.26 V coil drive
X mirror: deflects to +20° × (3071/4095) = +15°
Y mirror: deflects to −25% of max = −8.75°
Red laser diode: driven to 255/255 = 100% power
Spot on surface: centre-right and slightly below centre

## Key Performance Numbers
Parameter	Value	Source
MCU clock	112 MHz	SAM4S2B config
Max PPS (firmware)	65,535	MAXSPEED constant
Max PPS (practical)	30,000	default max_pps
SysTick period @ 30 kpps	33.3 µs	112M / 30k
SPI clock	22.4 MHz	112M / 5
Time for 4 SPI writes	~3 µs	4 × 16 bits @ 22.4 MHz
DACC settle time	~1 µs	SAM4S datasheet
Galvo small-signal bandwidth	~2–4 kHz	hardware
Galvo large-signal settle	5–15 ms	hardware — why dwell matters
Position resolution	12-bit (4096 steps)	DACC
Colour resolution	8-bit per channel	DAC084S085
Max frame size	4096 points	firmware buffer
USB latency (bulk transfer)	~2–8 ms	USB FS spec
Frame queue depth	2 frames	HeliosOutput cap
Effective galvo range	±20°–±40°	hardware

## Where Things Can Go Wrong
Symptom	Location	Cause
Circle chirps / flickers	BuildFrame starting pos	lastEndX_/Y_ was hardcoded center — every frame the galvo lurched back to center and re-travelled to circle start
Distorted corners	CalcCornerDwell	curve_threshold too high, dwell=0 at sharp angles
Dim endpoints / bright midpoints	ResampleToCount	Uneven arc-length resampling
Flickering on mode switch	DacThreadFunc queue	Frame queue not drained on stop
Chirping at specific angles	Galvo mechanical resonance	Scan rate × geometry producing resonant frequency
Frame drops / stuttering	SysTick vs USB priority	SysTick must be higher priority than USB
Galvo refuses to stop at centre	Delayed-stop timer (TC0)	100 ms guard delay before forcing blank/center